## Slide 1: Analog Reflector
Installation and Basic Setup

## Slide 2: How to Install on existing Debian Based System (ARM, i386, and AMD64)
Prerequisites: DVSwitch
Install the DVSwitch repository:
As root
  cd /tmp
  wget http://dvswitch.org/bustersudo chmod +x buster
  sudo ./buster
  sudo apt-get update
  sudo apt-get install dvswitch-server

## Slide 3: Configure Newly Installed DVSwitch
Setup MMDVM_Bridge
  Open MMDVM_Bridge.ini in your favorite text editor either via ssh or if you are like me, I prefer to use WINSCP and then open in Notepad++
  Located in /opt/MMDVM_Bridge/
  Set DMR ID +2Digit number ex: 123456701 USE YOUR OWN
  Make sure both frequencies are identical as shown
  [DMR Network] Stanza has a password, I am on Brandmeister mostly so if that’s the case, use your Self-Care Hostpot password.

## Slide 5
Brandmeister USA Servers

## Slide 6: Configure Newly Installed DVSwitch cont.
Setup Analog_Bridge
  Open Analog_Bridge.ini
  Located in /opt/Analog_Bridge/
  Set DMR ID and DMRID +2Digit number ex: 1234567 123456701 USE YOUR OWN
  This assumes you do not have a USB AMBE3000 Stick or Server so check the other highlighted areas.

## Slide 9: Configure Newly Installed DVSwitch Final
Run these commands
  systemctl enable mmdvm_bridge
  systemctl start mmdvm_bridge
  systemctl enable analog_bridge
  systemctl start analog_bridge
  systemctl enable md380-emu
  systemctl start md380-emu

## Slide 10: Analog_Reflector Install and Setup
apt update
apt upgrade
apt install analog-reflector
cd /opt/Analog_Reflector
cd ssl
./mkcerts.sh
Once mkcert completes, you have a self signed certificate for your host
cd /opt/Analog_Reflector
./Analog_Reflector user WG5EEK 3171240 317124003 password 11
systemctl enable analog_reflector
systemctl start analog_reflector
Point your browser at the server https://192.168.x.y and then enter your callsign and newly created password

## Slide 13: Analog_Reflector Bonus! Bridge to AllstarLink
Add/Replace 1999 Node Stanza right after your current Allstarlink Node Stanza, example: below [51010] in /etc/asterisk/rpt.conf
  https://dvswitch.groups.io/g/allstarlink/wiki/9671 <- Node Example

## Slide 14
Doublecheck your manager.conf password is setup in /etc/asterisk/manager.conf

## Slide 15: Analog_Relfector Bonus! Bridge to AllstarLink cont.
Enable USRP in modules.conf in /etc/asterisk/modules.conf
  Change noload => chan_usrp.so to load => chan_usrp.so

## Slide 16: Analog_Relfector Bonus! Bridge to AllstarLink cont.
Configure Analog_Reflector.json in /opt/Analog_Reflector/Analog_Reflector.json
amiSecret is the password from manager.conf under [admin]

## Slide 17: Analog_Relfector Bonus! Bridge to AllstarLink cont.
You should be able to connect to node 1999 from your main node but if it doesn’t work, you will have to add some lines in extensions.conf in /etc/asterisk/extentions.conf

## Slide 18: Analog_Relfector Bonus! Bridge to AllstarLink Final
You can either restart Asterisk in bash via astres.sh or via Supermon if setup and installed via the RESTART Button, or via the restart asterisk option in asl-menu, > 9 System Diagnostics Menu, G Restart ASL Asterisk.
You may just want to reboot

## Slide 19: Important Links
https://dvswitch.groups.io/g/Analog-Reflector/
https://dvswitch.groups.io/g/Analog-Reflector/files/Analog_Reflector.pdf
https://dvswitch.groups.io/g/allstarlink
https://dvswitch.groups.io/
https://news.brandmeister.network/configure-a-security-password-for-your-hotspots/
https://www.radioid.net/register#! <-Get a DMR ID