## Slide 1: What is SDR?

## Slide 2: Software Defined Radio
SDR is radio communications that are traditionally implemented in hardware such as mixers, filters, etc., but instead are now accomplished using software.
Beginnings in he 70s and 80s with DARPA and what is now Raytheon.
Really took off in the 90s with the USAF developing a system called SpeakEasy that had a goal of communicating from 2MHz to 2GHz covering 10 different radio protocols, encrypted and un-encrypted

## Slide 3: What about all of the USB dongles?
The origins of RTL-SDR stem from mass produced DVB-T TV tuner dongles that were based on the RTL2832U chipset. With the combined efforts of Antti Palosaari, Eric Fry and Osmocom (in particular Steve Markgraf) it was found that the raw I/Q data on the RTL2832U chipset could be accessed directly, which allowed the DVB-T TV tuner to be converted into a wideband software defined radio via a custom software driver developed by Steve Markgraf.
https://www.rtl-sdr.com/about-rtl-sdr/

## Slide 4: Popular Options

## Slide 5: What can I do with my $20 SDR stick?
Use as a police radio scanner.
Listening to EMS/Ambulance/Fire communications.
Listening to aircraft traffic control conversations.
Tracking aircraft positions like a radar with ADSB decoding.
Decoding aircraft ACARS short messages.
Scanning trunking radio conversations.
Decoding unencrypted digital voice transmissions such as P25/DMR/D-STAR.
Tracking maritime boat positions like a radar with AIS decoding.
Decoding POCSAG/FLEX pager traffic.
Scanning for cordless phones and baby monitors.
Tracking and receiving meteorological agency launched weather balloon data.
Tracking your own self launched high altitude balloon for payload recovery.
Receiving wireless temperature sensors and wireless power meter sensors.
Listening to VHF amateur radio.
Decoding ham radio APRS packets.
Watching analogue broadcast TV.
Sniffing GSM signals.
Using rtl-sdr on your Android device as a portable radio scanner.
Receiving GPS signals and decoding them.
Using rtl-sdr as a spectrum analyzer.
Receiving NOAA weather satellite images.
Listening to satellites and the ISS.
Radio astronomy.
Monitoring meteor scatter.
Listening to FM radio, and decoding RDS information.
Listening to DAB broadcast radio.
Listening to and decoding HD-Radio (NRSC5).
Use rtl-sdr as a panadapter for your traditional hardware radio.
Decoding taxi mobile data terminal signals.
Use rtl-sdr as a high quality entropy source for random number generation.
Use rtl-sdr as a noise figure indicator.
Reverse engineering unknown protocols.
Triangulating the source of a signal.
Searching for RF noise sources.
Characterizing RF filters and measuring antenna SWR.
Decoding Inmarsat STD-C EGC geosynchronous satellites.
Listening to the ISS (International Space Station).
Not all of these are legal in every country
WOW

## Slide 6: Police Scanner with Unitrunker
Unitrunker features
  Allows one SDR Dongle to monitor a trunked or simulcast system
  Supports routing audio through Virtual Cable
    Important because it allows decoding of audio with DSDPlus
  Supports Re-banded systems
  Can link with Radio Reference website if you have a paid account with them
  http://www.unitrunker.com/ Author Rickey Parrish KD4VXY (Expired in 2015)

## Slide 7: Unitrunker Settings
Set to 2 VCOs
(default is 3)
Choose your device

## Slide 8: Radio Reference
The system here only has four control channels so it isn’t too difficult to find the right one.

## Slide 9
Unitrunker Settings
Control Frequency
May or may not work

## Slide 10: Unitrunker Settings
Un-mute to listen to traffic

## Slide 11: Frequencies in use
Red shows control channel in use.
  This channel, at least here, switches between the other Control channels throughout the day.

## Slide 12: Rebranded
The system here uses the “Rebranded” configuration.
Read more here:
  https://wiki.radioreference.com/index.php/Rebanding
Select the Calculator Icon called Wizard
Click the Rebranded Tab
Close the Wizard window

## Slide 13: Advanced Configuration
Assign color to transmissions to differentiate between different services such as Law Enforcement, Emergency Medical Services, etc.
Should be automatically applied after download, unfortunately I don’t have an account to test this feature

## Slide 14: Unitrunker Demonstration Video

## Slide 15: SDR#

## Slide 16: SDR#
My goto SDR software
Made by Airspy
Supports multiple formats such as Wideband FM, Narrowband FM, Upper, Lower, and Dual Sidebands, and Carrier Wave.
Has a multitude of features to assist with audio filtering, decoding CTCSS (PL) and DCS codes
Can use as a radio scanner with a frequency manager plugin
Customizable waterfall similar to expensive ICOM, Yaesu, and Kenwood radios.
Plugins for just about every thing you can imagine

## Slide 17: SDR# Demonstration Video

## Slide 18: SDR# Quick GUI Overview

## Slide 19: Decoding Digital
Requirements
  Audio source from SDR# or any app that can output audio to a device of your choosing
  VBCable
  DSD Plus

## Slide 20: Decoding Digital
Install VBCable
Change sampling Rate in VBCable Control panel to 48000Hz
Restart PC
Change Audio Recording to
VB- Audio Virtual Cable
Uncheck Listen to this
Device

## Slide 21: Decoding Digital
Open and Extract both DSD Plus v1.01 and DLL files into the same folder
Run DSDPlus.exe
Run SDR# or equivalent and tune to DMR Frequency
  Turn off squelch and all audio filters
  Under Audio, select Output as the VB Cable Input

## Slide 22: DSD Plus in Action

## Slide 23: DSD Decoding Demonstration

## Slide 24: Tracking Aircraft with RTL1090
What it does
  Shows basic aircraft information
    Tail Number
    Call sign
    Altitude
    Speed
    Current Location
    Bearing
  Uses ADS-B data from aircraft
    Automatic Dependent Surveillance - Broadcast
  Author 90% certain it is:
  Günter Köllner DL4MEA

## Slide 25: Android SDR App
Online hosted SDR with multiple bands
Servers located worldwide

## Slide 26: WebSDR Demonstration

## Slide 27: Android Pocket RxTx
WebSDR for your phone
Uses same servers as WebSDR.org
Multiband receiver in your pocket
  Needs the Internet
Can control networked transceivers

## Slide 28: Android Pocket RxTx Demonstration

## Slide 29: What can I do with my $20 SDR stick?
Use as a police radio scanner.
Listening to EMS/Ambulance/Fire communications.
Listening to aircraft traffic control conversations.
Tracking aircraft positions like a radar with ADSB decoding.
Decoding aircraft ACARS short messages.
Scanning trunking radio conversations.
Decoding unencrypted digital voice transmissions such as P25/DMR/D-STAR.
Tracking maritime boat positions like a radar with AIS decoding.
Decoding POCSAG/FLEX pager traffic.
Scanning for cordless phones and baby monitors.
Tracking and receiving meteorological agency launched weather balloon data.
Tracking your own self launched high altitude balloon for payload recovery.
Receiving wireless temperature sensors and wireless power meter sensors.
Listening to VHF amateur radio.
Decoding ham radio APRS packets.
Watching analogue broadcast TV.
Sniffing GSM signals.
Using rtl-sdr on your Android device as a portable radio scanner.
Receiving GPS signals and decoding them.
Using rtl-sdr as a spectrum analyzer.
Receiving NOAA weather satellite images.
Listening to satellites and the ISS.
Radio astronomy.
Monitoring meteor scatter.
Listening to FM radio, and decoding RDS information.
Listening to DAB broadcast radio.
Listening to and decoding HD-Radio (NRSC5).
Use rtl-sdr as a panadapter for your traditional hardware radio.
Decoding taxi mobile data terminal signals.
Use rtl-sdr as a high quality entropy source for random number generation.
Use rtl-sdr as a noise figure indicator.
Reverse engineering unknown protocols.
Triangulating the source of a signal.
Searching for RF noise sources.
Characterizing RF filters and measuring antenna SWR.
Decoding Inmarsat STD-C EGC geosynchronous satellites.
Listening to the ISS (International Space Station).
Not all of these are legal in every country
WOW

## Slide 30: Links
DSD Plus https://www.dsdplus.com/download-2/
VBCABLE https://www.vb-audio.com/Cable/
SDR# https://airspy.com/download/
RTL1090 https://rtl1090.com/
WebSDR http://www.websdr.org/